## Slide 2: Overview of the Internet
Network
LAN
WAN
    Point-to-point WAN
    Switched WAN
Switching
Circuit-switched Network
Packet-switched Network

## Slide 3: Accessing the Internet
Using telephone Networks
    Dial-up Service
    DSL service
Using Cable Networks
Using Wireless Networks
Hardware and software
H/w and S/W are coordinated with each other using protocol layering.

## Slide 4: Protocol Layering
Protocol defines the rules that both the sender and receiver and receiver and all the intermediate devices need to follow to be able to communicate effectively.

## Slide 5
A three layer protocol

## Slide 6: TCP/IP Protocol Suite

## Slide 7: Layers in TCP/IP Protocol
Application Layer
      Process-to-process communication
      HTTP
      SMTP
      FTP
      Telnet
      SSH
Transport Layer
      Consists of two protocols
      TCP and UDP

## Slide 8: Layers in TCP/IP Protocol
Network Layer
        IP
        ICMP
        IGMP
        DHCP
        ARP
Datalink Layer
        -moving datagram across link
        -error detection & correction
Physical Layer

## Slide 9: Encapsulation and Decapsulation
Encapsulation at Source host
Decapsulation and Encapsulation at router
Decapsulation at the Destination.

## Slide 10: Addressing

## Slide 11: MULTIPLEXING AND DE-MULTIPLEXING
FTP
HTTP
DNS
SNMP
TCP
UDP
IP
MULTIPLEXING

## Slide 12
FTP
HTTP
DNS
SNMP
TCP
UDP
IP
DEMULTIPLEXING

## Slide 13: OSI MODEL

## Slide 14: Telnet
A generic client/server program that allows clients to login into the server system and uses services provided by the server.
Instead of installing costly s/w I will use that provided in the server , pay for my use.
TELNET-TERMINAL NETWORK is one of the original (oldest) remote login application.
It is vulnerable to attacks, it is almost replaced by SSH, Secure Shell but it is still used for two reasons
  for its simple architecture
  Good for using as diagnostic and debugging tool.

## Slide 15: Telnet
Local versus remote logging
Local –Operating system translates the characters and opens desired utility
Remote-the user enter the keystroke( user name and passwd , the keystroke is sent to local OS, which sends it to Telnet client which converts it to NVT char set.
The TCP/IP at server gives this set to OS , then OS to Telnet server which translates NVT to char set which can be under stood by its system
OS does not directly receives the data, it receives from pseudo terminal.

## Slide 16: TELNET

## Slide 17: NVT
N/W consists for heterogeneous systems.
Via NVT interface , translation of character set from client to NVT form and at server from NVT form to remote system form.

## Slide 18: SSH
SSH in application has three components running on top of TCP.
  SSH transport-layer protocol
  SSH authentication protocol
  SSH connection protocol
APPLICATION
SSH-CONN
SSH-AUTH
SSH-TRANS
TCP

## Slide 19: SSH
SSH is a general purpose protocol.
Unique se rvices provided by ssh is port forwarding.

## Slide 20: DNS (Domain name server)
Maps names to numbers
Converts www.example.com to 172. 59.10.16
The following six steps map hostname to IP address
1. The user passes the host name to the file transfer client.
2. The file transfer client passes the host name to the DNS client.
3. each computer after being booted, knows the address of one DNS server. The DNS client sends a message to a DNS server with
a query that gives the file transfer server name using the known IP address of the DNS server.
4. The DNS server responds with the IP address of the desired file transfer server.
5. The DNS client passes the IP address to the file transfer server.
6. The file transfer client now uses the received IP address to access the file transfer server.

## Slide 21: DNS

## Slide 22: DNS
A name space that maps each address to a unique name can be organized in two ways:
flat or hierarchical.
A namespace in flat is a sequence of characters without any structure. This cannot be used in Internet.
In Hierarchical each name has several parts, like first part may indicate nature of the organization, second part may indicate name of the organization , third part may indicate different departments in organization.
The name giving authority can sometimes define only name and nature of the organization and can give the liberty of defining rest of the names to the organization itself.
Suppose two organization wants same name, Julius, so name authority gives first and second as names is organization, then organization can add prefixes or postfixes to make the name unique. like julius.first.com, julius.second.com.

## Slide 23: DNS

## Slide 24: DNS

## Slide 25: DNS

## Slide 26: DNS
Primary Server
Secondary Server

## Slide 27: DNS in INTERNET
Generic Domains
Country Domains
Inverse Domains( not used now)
        Generic Domain

## Slide 28: DNS in INTERNET
Country Domain

## Slide 29: DNS Resolution
Recursive Resolution

## Slide 30: DNS Resolution
Iterative Resolution

## Slide 31: DNS CACHING
A Resource record consists of 5-tuple
(domain name, type, class, TTL, value)

## Slide 32: DNS
DNS msg structure
Registrars
DDNS
Security of DNS